## Slide 1: GDA2020 update ISO / EPSG / GMIWG
ANZ Metadata Working Group
23 March 2020
Melbourne / Remote
Joel Haasdyk
GDA2020 Program Manager, NSW
Department of Customer Service, NSW

## Slide 2: Content
1) ANZLIC 30 June 2020 Deadline for FSDF delivery
Legislation updates (e.g. NSW commenced 01 January 2020)
2) ISO 19115-1 amendment pending (time-dependence)
3) EPSG changes pending;
IOGP & Australian actions
4) GMIWG actions/ GMIWG requests to ANZ MD WG.
23 MAR 2020 - GDA2020 update – ANZ MD WG

## Slide 3: ISO 19115-1 amendment pending RE time-dependence)
To require CRS (or referenceSystemIdentifier) [Not previously required??]
To require Coordinate Epoch, if CRS = dynamic
  Q) Where must ‘CRS = dynamic’ definition be defined?
Timing anticipated for amendment (advice received 15/03):
  ISO secretariat deems these changes to be ‘technical, therefore longer process:
  8 week FDIS ballot => 12 week FDIS ballot (+ possibly further 2 months for language translations)
Related metadata requirements:
  Lineage (Process steps)
  Other ‘epoch(s)’ (per previous report to ANZ MD WG Oct 2019)
  zarina.jayaswal@defence.gov.au “+ Shanti” request for more information (20/03/2020):
    “Can you please let me know what meta data we need stored regarding datum, … seems to have been missed in the latest ISO standard.”
    Drafting doc: “Why there is a need for separate metadata fields for epochs.
23 MAR 2020 - GDA2020 update – ANZ MD WG

## Slide 4: EPSG changes, recent IOGP meetings (limited)
‘Ensemble’ CRS, consisting of multiple similar member CRS:
e.g. WGS ensemble (EPSG CRS codes 4326, 4978 and 4979) contains members:
[Transit, G730, G873, G1150, G1674 and G1762]
Currently only ensembles in EPSG are WGS84 and ETRS89.
  Even if an ensemble’s members are dynamic, e.g. WGS84(G1762) EPSG:7665, etc = dynamic
  Ensemble itself = static e.g. WGS84 EPSG:4326, etc = static
    WGS84 @ epoch is not valid
    but WGS84(G1762) @ epoch is valid, but WGS84(G1762) rarely used vs WGS84 ensemble
  Documentation to come from IOGP.
  “the act of using such an ensemble implies that the user is ignoring plate motion”
  “This interpretation of ensembles being low accuracy (because they ignore tectonic movement) is consistent with the unofficial position of Google and possibly other web-mapping providers, but that was not an issue considered in our decision-making.”
23 MAR 2020 - GDA2020 update – ANZ MD WG

## Slide 5: EPSG changes, (continued…)
HOWEVER….
It is perfectly valid to define time-dependent transformation between:
  Dynamic <> Dynamic datums e.g. ITRF2014 <> ITRF1992
  Dynamic <> Static Datums e.g. GDA2020 <> ITRF2014;
  Static <> Static Datums e.g. GDA2020 <> WGS84; NAD83 <> GDA2020
Australia to submit for new EPSG codes:
  New GDA2020 <time-dependent> WGS84
  New GDA94 <time-dependent> WGS84
  Also cater for AGD66 (within ACT…)
  Note: these will NOT replace existing codes (difficult to deprecate what is already in the wild)
23 MAR 2020 - GDA2020 update – ANZ MD WG

## Slide 6: GMIWG intention / request to ANZ MD WG
GMIWG intends additional Fact Sheets: https://www.icsm.gov.au/datum/gda2020-fact-sheets
  WGS84 and time-dependence / EPSG changes.
  ? Metadata Fact Sheet ?
GWIMG requests (noting ISO19115 update pending, 3-6 months minimum)
  ISO19139 => ISO 19115 drivers? Fact Sheet? ’Best Practice Guideline’
  Examples / advice:
    How to indicate ‘lineage’? i.e. Source => Transformation => Storage
    How to indicate ‘GDA2020 compliant’ vs ‘GDA2020 compatible (insignificant difference)’ https://www.icsm.gov.au/gda2020/using-gda2020-logo
  (?) Updated ANZLIC Metadata Tool (earlier comment “Tools/Templates, not standards”)
  Aside: AS5488:2019, doesn’t currently define Datum. 2nd Review pending.
23 MAR 2020 - GDA2020 update – ANZ MD WG

## Slide 7: Reference slides below
23 MAR 2020 - GDA2020 update – ANZ MD WG

## Slide 8: Notes on epoch(s) definitions.
‘Coordinate Epoch’: [per ISO 19111:2019] Epoch to which coordinates in a dynamic coordinate reference system are referenced
Observation Epoch / Temporal Extent: [Per ISO xxxx]: Epoch(s) at which data is physically observed / captured.
Reference Epoch: [defined where?]: Used to distinguish one CRS realisation from another. E.g. ITRF2008 vs ITRF2014; Nominally represents date of the last data employed in creating the realisation.
‘Frame Reference Epoch’: [per ISO 19111:2019]: “Epoch of coordinate that define a dynamic reference system.” [JH comment: Is this equivalent to Realisation Epoch, above?]
‘Parameter Reference Epoch’ and/or “Transformation Reference Epoch”: [per ISO 19 111:2019]: “Epoch at which the parameter values of a time-dependent coordinate transformation are valid
Note 1 to entry: The transformation parameter values first need to be propagated to the epoch of the coordinates before the coordinate transformation can be applied.” [OR Coordinates transformed to the transformation epoch.]
Note: Some of the above need clarification / consistency:
e.g. http://www.epsg-registry.org/ will provide “Realization epoch: 2010-01-01” for ITRF2014 (EPSG:9000, 7912)
I would call this a “Parameter Reference Epoch”
23 MAR 2020 - GDA2020 update – ANZ MD WG

## Slide 9
Use Case | CRS | Coordinate Epoch1 | Observation Epoch2 [or Range] [vs Temporal Extent = approx?]
Observe Data in ATRF (GPS at 3-10cm accuracy in Australia | ATRF2014 ‘2014’ 3 nominal from ITRF2014 Defined as coordinates at epoch 2020.0 4, plus velocities | @today Equal to Observation epoch Precision driven by user need 2019.83 or 2019.82543 or 2019/10/28 14:05:18 Single epoch only; [average?] Data-set level metadata only? | @today , for example: 2019/10/28 2019/10/28 14:05:18 2019/10/28 14:05:18 – 15:06:30 Time range, rarely an instance Can only be extent in metadata and/or timestamp on each point.
Propagate to a project epoch e.g. for storage(?), analysis | ATRF2014 | @projectEpoch (e.g. 2015.0) via velocities / models | @today (unchanged)
Transform to CRS2 | GDA2020 | [@2020.0; implicitly] | @today (unchanged)
Transform to CRS3 | ITRF2014 Defined as coordinates at epoch 2010.0 , plus velocities | @anyEpoch (e.g. 2023.54) | @today (unchanged)
Coordinate Epoch – Example Use Cases
Velocity Model + Accuracy
Transform + accuracy
Parameters are time-dependent! 5
Transform + accuracy:
Parameters are time-dependent! 5
1 “Coordinate Epoch” Epoch at which the data is described in the nominated CRS. Explicitly required for a dynamic CRS> Best described by ISO8601? ISO19108? Decimal year? Extensible to enable user defined precision? Single epoch… average(?) of recorded Observation epoch(s) if a range.
2 “Observation Epoch” Epoch at which the data is physically observed.
3 “Realisation [Epoch]” Date nominated to distinguish one CRS realisation from another. E.g. ITRF2008 vs ITRF2014; Nominally last data employed in creating the realisation.
4 “Frame Reference Epoch” Epoch of Coordinate that define a dynamic reference system [ISO 19111:2019]
5 “Parameter Reference Epoch” and /or “Transformation Reference Epoch”: Transformations between dynamic CRSs are time-dependent [ISO 19111:2019]
Copy from Oct 2019 presentation to ANZ MD WG;’ Possible superseded
23 MAR 2020 - GDA2020 update – ANZ MD WG

## Slide 10
Use Case | CRS: | Coordinate Epoch1 | Observation Epoch2 [or Range] [vs Temporal Extent = approx]
Observe from GPS (without local differential ystem) | WGS84 [which? – WGS84 is an ensemble at metre-level] | @today Equal to Observation epoch(s), | @today
Observe GPS (via CORS network) | CORS-defined CRS | CORS-defined Epoch | @today
Coordinates obtained from website / web-service | WGS84? [if so, which?] Per metadata from service? Unknown? | Per metadata from service ? Unknown? | Per metadata from service? Date of new capture? Unknown?
Coordinate from Imagery | Per metadata from service? Unknown? | Per date of image capture? Per date of image CRS? Unknown? | Per date of image capture? Date of new capture? Unknown?
Coordinate Epoch – Example Use Cases
Copy from Oct 2019 presentation to ANZ MD WG;’ Possible superseded
23 MAR 2020 - GDA2020 update – ANZ MD WG

## Slide 11: WGS84 / Web-mercator: WGS84 needs a time-stamp!
“Why are my maps out by 1.8 meters?”
1994
2020
‘Web-Mercator’
Null
(no change)
Null
(no change)
1.8 m
‘Web-Mercator’
23 MAR 2020 - GDA2020 update – ANZ MD WG
Notes: In Australia we have been receiving calls from GIS users asking us why their maps are now misaligned by 1.8 metres.
For instance,..
Meet “Julie”
Julie is a GIS officer in a local council.
Keep in mind she’s been in the job for 6 months, isn’t paid very much, and is the coal-face of this issue. She is the one expected to make it all work, and to explain up the chain when something is going wrong.
Julie was layering map features from ESRI portal over a basemap WMS from Nearmap.
The features (in WGS84) were aligned with our old national datum, and basemap, (also in WGS84) was aligning maps with our new datum.
By definition, that is supposed to be okay.
But 1.8 metre misalignment is not okay for a local council.
This map-misalignment problem we are experience is the Y2K problem of mapping.
The shortcuts our mapping community previously took with web-mapping are breaking Australia’s datum modernisation program.

## Slide 12: WGS84 / Web-mercator: WGS84 needs a time-stamp!
“Why are my maps out by 1.8 meters?”
1994
2020
‘Web-Mercator’
1.8 m
Null transform
(no change)
WGS84 @ today
23 MAR 2020 - GDA2020 update – ANZ MD WG
Notes: In Australia we have been receiving calls from GIS users asking us why their maps are now misaligned by 1.8 metres.
For instance,..
Meet “Julie”
Julie is a GIS officer in a local council.
Keep in mind she’s been in the job for 6 months, isn’t paid very much, and is the coal-face of this issue. She is the one expected to make it all work, and to explain up the chain when something is going wrong.
Julie was layering map features from ESRI portal over a basemap WMS from Nearmap.
The features (in WGS84) were aligned with our old national datum, and basemap, (also in WGS84) was aligning maps with our new datum.
By definition, that is supposed to be okay.
But 1.8 metre misalignment is not okay for a local council.
This map-misalignment problem we are experience is the Y2K problem of mapping.
The shortcuts our mapping community previously took with web-mapping are breaking Australia’s datum modernisation program.

## Slide 13: WGS84 / Web-mercator: WGS84 needs a time-stamp!
“Why are my maps out by 1.8 meters?”
1994
2020
‘Web-Mercator’
1.8 m
Null transform
(no change)
WGS84 @ today
WGS84 needs a time-stamp!
GDA94 ► WGS84@1994.0 GDA2020 ► WGS84@2020.0
GPS handheld ► WGS84@today
NSW Spatial Services
“WGS84 = WGS84@1994.0”
23 MAR 2020 - GDA2020 update – ANZ MD WG
Notes: In Australia we have been receiving calls from GIS users asking us why their maps are now misaligned by 1.8 metres.
For instance,..
Meet “Julie”
Julie is a GIS officer in a local council.
Keep in mind she’s been in the job for 6 months, isn’t paid very much, and is the coal-face of this issue. She is the one expected to make it all work, and to explain up the chain when something is going wrong.
Julie was layering map features from ESRI portal over a basemap WMS from Nearmap.
The features (in WGS84) were aligned with our old national datum, and basemap, (also in WGS84) was aligning maps with our new datum.
By definition, that is supposed to be okay.
But 1.8 metre misalignment is not okay for a local council.
This map-misalignment problem we are experience is the Y2K problem of mapping.
The shortcuts our mapping community previously took with web-mapping are breaking Australia’s datum modernisation program.

## Slide 14: WGS84 / Web-mercator: WGS84 needs a time-stamp!
“Why are my maps out by 1.8 meters?”
1994
2020
‘Web-Mercator’
1.8 m
WGS84 needs a time-stamp!
GDA94 ► WGS84@1994.0 GDA2020 ► WGS84@2020.0
GPS handheld ► WGS84@today
Time
Time
WGS84
WGS84 @ today
Long-term solution:
Treat WGS84 as a dynamic datum
Record ‘Coordinate Epoch’ (for all dynamic datums)
ISO 19111
ISO 19115
EPSG
‘static’
‘dynamic’
v10.0
AUS
Software => ATRF…
NSW Spatial Services
“WGS84 = WGS84@1994.0”
23 MAR 2020 - GDA2020 update – ANZ MD WG
Notes: In Australia we have been receiving calls from GIS users asking us why their maps are now misaligned by 1.8 metres.
For instance,..
Meet “Julie”
Julie is a GIS officer in a local council.
Keep in mind she’s been in the job for 6 months, isn’t paid very much, and is the coal-face of this issue. She is the one expected to make it all work, and to explain up the chain when something is going wrong.
Julie was layering map features from ESRI portal over a basemap WMS from Nearmap.
The features (in WGS84) were aligned with our old national datum, and basemap, (also in WGS84) was aligning maps with our new datum.
By definition, that is supposed to be okay.
But 1.8 metre misalignment is not okay for a local council.
This map-misalignment problem we are experience is the Y2K problem of mapping.
The shortcuts our mapping community previously took with web-mapping are breaking Australia’s datum modernisation program.