## Slide 1: Preparing metadata for GDA2020 and the AGRS ANZ Metadata Working Group Meeting No 7
29-31 July 2020
Virtual meeting
Irina Bastrakova, Joel Haasdyk, Byron Cochrane

## Slide 2: Upgrades to the Australian Geospatial Reference System (AGRS)
Concerns providers and users of spatial data
Includes:
Geocentric Datum of Australia 2020 (GDA2020)
Australian Terrestrial Reference Frame (ATRF)
Australian Vertical Working Surface (AVWS)
More information: https://www.icsm.gov.au/upgrades-australian-geospatial-reference-system

## Slide 3: Geocentric Datum of Australia 2020 (GDA2020)
GDA2020 is a static datum – just like GDA94
Positions of features (e.g. roads) do not change over time
GDA94 to GDA2020 differences will range in size from ~1.5 to 1.8m due to tectonic plate motion and ~1.3 to 2.3m when include regional GDA94 definitions
GDA2020 spatial data is more closely aligned to Global Navigation Satellite Systems (e.g. GPS) to benefit from modern positioning technology
GDA2020 has been available for use since 17 October 2017
Transform between GDA94 and GDA2020 using transformation parameters or grids1
Models and documentation are at https://www.icsm.gov.au/publications

## Slide 4: Australian Terrestrial Reference Frame 2014 (ATRF2014)
The ATRF2014 is a time dependent reference frame
A ‘time-dependent reference frame’ (a.k.a. ‘dynamic datum’,) is used to describe features whose coordinates change with time, e.g. due to plate tectonic motion
GNSS operates in a time-dependent reference frame
ATRF2014 coordinates for a feature will change with time as the Australian tectonic plate moves
Coordinates expressed in ATRF2014 require a time-stamp in order to be unambiguous
ATRF2014 is expected to be used for Intelligent Transport Services (e.g. autonomous vehicles), Location Based Services (e.g. mobile applications), or by the scientific community
ATRF2014 has been available for use since 1 January 2020
Users can propagate ATRF2014 coordinates through time using the Australian Plate Motion Model: https://www.icsm.gov.au/publications

## Slide 5: Australian Vertical Working Surface (AVWS)
AVWS is a new reference surface for heights in Australia without the bias and distortion present in the Australian Height Datum (AHD)
AVWS heights can be computed from GNSS ellipsoidal heights through application of the Australian QuasiGeoid Model with accuracy of 4-8 cm
AVWS has been available for use since 1 January 2020
For information about Australian Plate Motion Model: https://www.icsm.gov.au/publications

## Slide 6: ISO 19111 Coordinate Operations
200 m
30 JUL 2020 – GDA2020 – ANZ MD WG
1.8 m
AGD66
GDA94
GDA2020
Map Grid AMG66
Map Grid MGA94
Map Grid MGA2020
Conversion
Change in Units
Point Motion
Change over time
Transformation
Change in CRS definition
ATRF@epoch
Notes: In Australia we have been receiving calls from GIS users asking us why their maps are now misaligned by 1.8 metres.
For instance,..
Meet “Julie”
Julie is a GIS officer in a local council.
Keep in mind she’s been in the job for 6 months, isn’t paid very much, and is the coal-face of this issue. She is the one expected to make it all work, and to explain up the chain when something is going wrong.
Julie was layering map features from ESRI portal over a basemap WMS from Nearmap.
The features (in WGS84) were aligned with our old national datum, and basemap, (also in WGS84) was aligning maps with our new datum.
By definition, that is supposed to be okay.
But 1.8 metre misalignment is not okay for a local council.
This map-misalignment problem we are experience is the Y2K problem of mapping.
The shortcuts our mapping community previously took with web-mapping are breaking Australia’s datum modernisation program.

## Slide 7: AGRS definitions recommended for lineage metadata
GDA2020 Compliant vs Compatible data
  GDA2020 Compliant refers to spatial data:
    observed directly in GDA2020
    transformed to GDA2020 in accordance with the GDA2020 Technical Manual
  GDA2020 Compatible refers to spatial data:
    low accuracy (3 m or poorer)
    Difference between nominated reference system and GDA2020 is insignificant
Coordinate Operations
  Coordinate operation:
    A process using a mathematical model, based on a one-to-one relationship, that changes coordinates in a source CRS to coordinates in a target CRS, or that changes coordinates at a source coordinate epoch to coordinates at a target coordinate epoch within the same CRS
  Coordinate conversion:
    A coordinate operation that changes the coordinates in a source CRS to coordinates in a target CRS based on the same datum. This does not represent a change to the coordinates of the described feature, but rather a different representation of the same coordinate
  Coordinate transformation:
    A coordinate operation that changes coordinates in a source CRS to coordinates in a target CRS in which the source and target CRS are based on different datums
  Point motion operation:
    A coordinate operation that changes coordinates within one CRS due to the motion of the point
  Concatenated operation:
    A coordinate operation consisting of the sequential application of multiple coordinate operations

## Slide 8: Reference Systems
Class | Element | Definition | Comments
Reference System |  | Information about reference system | The reference system enables users to record information about spatial (horizontal and vertical) datums, projections and/or temporal systems for spatial, temporal or spatiotemporal datasets, including the code, description, code space, authority and URL linking to descriptions of reference systems
 | Reference System Identifier | Identifier for reference system | Specify the code, authority and URL of this authority, e.g. reference to the Geodetic CRS (geographic 2D) for GDA2020will be recorded as EPSG:7844 http://www.epsg-registry.org.
 | Reference System Type | Type of reference system | Specify what reference system type the identifier belongs to: temporal, vertical, etc. e.g. the type of example above will be ‘geodeticGeographic2D’

## Slide 9: Temporal Extent & Reference System (Coordinate Epoch)
Class | Element | Definition | Comments
Reference System (Coordinate Epoch) |  | Information about the Coordinate epoch | Recording the Coordinate Epoch is important for propagating coordinates through time when data is gathered on a dynamic datum such as the Australian Terrestrial Reference Frame (ATRF2014)
 | Reference System Identifier | Code - Identifier for the Coordinate Epoch | Specify the Coordinate Epoch of the data in decimal year to at least two places.
 |  | Description - of the Coordinate Epoch reference | Values - “Coordinate Epoch – *type of reference system*”
 | Reference System Type | Type of reference system | Coordinate Epoch has reference system type of ‘temporal’
Temporal Extent |  | Provides temporal component of the extent of the referring object | Data observation time: time or time period when data was collected or observed. Can be represented as a single datetime or a range (start and end datetime).

## Slide 10: History of acquisition & transformations - Lineage
Class | Element | Definition | Comments
Lineage |  | Information about the events or source data used in constructing the data or lack of knowledge about them | Record of history of the data lifecycle, including processing steps and transformations; Link to the source data metadata where possible
 | Statement | General explanation of the data producer’s knowledge about the data history | Record of history of data generation or transformation, including accuracy/uncertainty of data.
 | Process steps | Structured details of an event or transformation in the life of data including the process used to maintain data | Record of procedure(s) of data generation or transformation in a structured way
 | Source | A link to metadata or records information about the source data used in creating the data specified by the scope | Recording information about source data used in creating a dataset helps to better understand and access data quality and fitness for purpose

## Slide 11
Preparing metadata for GDA2020 and the AGRS available at
ICSM - Metadata Working Group web pages